## Slide 1
Industrial Ecology open online course (IEooc)
Part II: Methods
Methodology 2: Basics of material flow analysis (MFA)
IEooc_Methods2_Lecture4
Process inventories, product systems, life cycle indicators, footprints, and emissions scopes
Stefan Pauliuk, University of Freiburg, Germany

## Slide 2: The life cycle perspective on products and services Direct and indirect emissions

## Slide 3
The product life cycle – A subset of society’s metabolism
https://steelemotive.world/life-cycle-assessment-for-vehicle-development/
The product life cycle is a system that includes the proceses, stocks and flows of
the entire supply chain of a product,
its use phase and the emissions from the use phase,
the supply chain of the operational energy and matrial flows for the use phase,
the end-of life treatment and recycling stages.

## Slide 4
Life cycle impacts – GHG emissions scopes
https://www.lifecycleinitiative.org/starting-life-cycle-thinking/life-cycle-approaches/carbon-footprint/

## Slide 5
Life cycle impacts – GHG emissions scopes
https://www.lifecycleinitiative.org/starting-life-cycle-thinking/life-cycle-approaches/carbon-footprint/
● Scope 1 – Direct GHG emissions – these occur from sources that are owned or controlled by the company, for example emissions from combustion in owned or controlled boilers, furnaces, vehicles, etc. or emissions from chemical production in owned or controlled process equipment.
● Scope 2 – Electricity and heat indirect GHG emissions – this accounts for GHG emissions from the generation of purchased electricity and heat consumed by the company. Purchased electricity is defined as electricity that is purchased or otherwise brought into the organizational boundary of the company. Scope 2 emissions physically occur at the facility where the electricity is generated.
● Scope 3 – Other indirect GHG emissions – this is a reporting category that allows for the treatment of all other indirect emissions. Scope 3 emissions are a consequence of the activities of the company, but occur from sources not owned or controlled by the company. Some examples of Scope 3 activities are the extraction and production of purchased materials, the transportation of purchased fuels and the use of sold goods and services.

## Slide 6: The life cycle perspective on products and services process inventories and process-level indicators

## Slide 7
For studying interactions along the energy service cascade, we need to quantify
processes on multiple layers of quantification: energy, mass, product, water, ..
Multi-layer process descriptions: A general MEFA tool
Process with stock, region, time
(example)
10 Mt steel
2.8 Mt CO2
3 Mt slag
mass output
emissions/
waste:
mass input
product input
1000 GPS
devices
2000 side mirrors
8 Mt steel coils
2 Mt plastics
4000 car seats
product output
energy input
(can be linked to mass flow,
like carbon in coal)
Products,
materials
The different layers of the process description are coupled by parameters
(material per product, energy per material, GHG per energy, …)
Only the necessary mass and energy balances are established!
(save time, don’t determine flows that are not relevant for problem at hand)
1000 cars
400 GJ electricity
180 GJ nat. gas

## Slide 8
Flows normalized per main output: The unit process
Unit Process:
Primary steel production,
Germany, 2008
1 t steel
2.8 t CO2
300 kg slag
Main product:
Emissions/
Waste:
Precursor
products
Natural
resources
260 kg O2
1.5 t iron
ore
945 kg Coke
1800 kWh Electr.
400 kg Limestone
Each industrial process is assigned one main product.
Flows are recorded in ‘natural’ physical unit.
Accounting on multiple physical layers.
Take process inventory and normalize it to 1 unit of main product
(here: by dividing all flows by 10 million)

## Slide 9
Example: Inventory of an industrial process
Primary steel production,
Company X
Germany, 2013
10 Mt steel
2.8 Mt CO2
3 Mt slag
Main product:
Emissions/
Waste:
Precursor
products
Natural
resources
2.6 Mt O2
15 Mt iron
ore
9.45 Mt Coke
1.8 TWh Electr.
4 Mt Limestone
Flows are recorded in ‘natural’ physical unit, using data from company records
and process models
Accounting on multiple physical layers, therefore only basic mass and energy
balance checks possible.
System boundary: Integrated steel mill of company X, Duisburg, Germany
annual total, 2013

## Slide 10
Sometimes called ‘direct’ indicators, as only quantities that are directly
connected to the process are considered.
- Most important example: Efficiency and loss rates, emissions factor
Basic process, product, and per capita indicators
Energy conversion process
Ein (e.g., fuel)
EL (losses)
Euseful (e.g., motion)
We define:
Efficiency: e := useful output / total input = Euseful /Ein
Loss rate: l := total loss / total input = EL /Ein
Works for: mass (mass yield, yield loss rate), energy (energy efficiency, energy loss rate),
Efficiency and loss rates are always >= 0 and <= 1.
More indicators: see the lectures on renewable energy indicators

## Slide 11
Central transport example:
Specific vehicle fuel consumption f
in MJ/ km or fV in l/100 km
Basic process, product, and per capita indicators
Internal combustion engine vehicle
Vin , Ein (e.g., fuel)
EL (losses)
Euseful (e.g., motion)
https://www.carsguide.com.au/car-advice/official-vs-real-world-fuel-consumption-figures-why-do-they-differ-39597
f in l/100 km, as declared
by manufacturer
f in l/100 km, from actual
driving cycle
difference in %
Suseful (e.g., driving)
f = Ein / Suseful
fV = Vin / Suseful

## Slide 12: The life cycle perspective on products and services Product system Life cycle indicators Footprints

## Slide 13
The product system of a product or service
https://en.wikipedia.org/wiki/Life-cycle_assessment
The product system of a product or service is a collection of processes (activities that transform inputs to outputs) and flows between them that are needed to perform a specified function and are within the system boundary of the study. It is the set of all the processes and exchanges that are part of the life cycle of a product or service.
Cut here for product-focussed system: ‚Cradle to gate‘
Whole system shown for service-focussed system: ‚Cradle to grave‘
Inputs of materials, energy, or water for process operation
Outputs of waste for treatment or disposal

## Slide 14
Quantifying product systems
Iron ore smelting
Steel making
Engine manufacturing
Car assembly
System definition: Life cycle of a passenger vehicle, energy, material, and product flows
ES
EL1
EL2 (losses)
EMa
M1 (pig
iron)
M2
(Steel)
M3
(engine)
PCar
Aluminium production
EL4 (losses)
M3a (Al)
Glass production
EL5(losses)
EG
ESt
EAl
Vehicle use
EL3
E6(fuel)
EL6(losses)
PEoL
(End-of
Life
vehile)
Vehicle recycling
EL7 (losses)
E7(recycling)
Example: Product system of cars / driving (very rough):
Production phase: cradle to gate
Use phase
EoL phase:
Grave
Energy supply
EAl , EMa , …
Final disposal
Shown in figure above:
Most flows of materials and energy
Flows of components and products
Not shown in figure above but included (too much…)
Natural resource input: raw materials, water, air
Emissions to nature (other than heat loss): GHG, waste, …
Product systems quickly become very large (1000s of materials, components, global supply chains, recycling, …)
In the MEFA class, we study small and simplified systems only
In the supply chain & life cycle mgt. classes, you will learn how to build product systems from process databases.

## Slide 15
Product system indicators: Embodied energy, GHG, water, …
Iron ore smelting
Steel making
Engine manufacturing
Car assembly
System definition: Life cycle of a passenger vehicle, energy, material, and product flows
ES
EL1
EL2 (losses)
EMa
M1 (pig
iron)
M2
(Steel)
M3
(engine)
PCar
Aluminium production
EL4 (losses)
M3a (Al)
Glass production
EL5(losses)
EG
ESt
EAl
Vehicle use
EL3
E6(fuel)
EL6(losses)
PEoL
(End-of
Life
vehile)
Vehicle recycling
EL7 (losses)
E7(recycling)
Example: Product system of cars / driving (very rough):
Production phase: cradle to gate
Use phase
EoL phase:
Grave
Energy supply
EAl , EMa , …
Final disposal
The embodied final/primary energy, GHG, water, or raw material of a product or service:
Embodied energy of product: Eeb := system-wide input of energy in production phase = ES + ESt + EMa + EAl + EG
Embodied GHG of product: GHGeb := system-wide GHG emissions from production phase (not shown above)
Embodied xyz of service: The above plus flows from the use and end-of-life (EoL) phases. For example:
Embodied energy of driving: ELifecycle := system-wide input of energy = ES + ESt + EMa + EAl + EG + E6 + E7
Works for all quantities that cross the system boundary (no double-counting in that case) and for final energy
consumed in the different process steps.
Scope 1 (direct indicators)

## Slide 16
System boundaries, scopes, & indicators for services...
...must be used consistently!
Use phase
scope 1 impact
of the service
Service
GHG, …
End-of-life, waste mgt.
scope 3 impact
of the service
GHG, …
Energy & heat suppl.
scope 2 impact
of the service
GHG, …
Water
PE
Materials, upstream
GHG, …
Water
PE
scope 3 impact
of the service
Terminology:
Life cycle X (PE, Water, GHG, raw materials) of service
=
Embodied X of service
=
X Footprint of service
=
cradle (nat. resources) to grave (landfill) X of service (only if disposed of at EoL)
=
cradle to cradle X of service (if recycling or re-use is included)
=
X(scope 1) + X(scope 2) + X(scope 3)

## Slide 17
The product life cycle for vehicles and the fuel supply: System boundaries and indicators for driving as a service
https://www.researchgate.net/figure/Illustration-of-a-vehicle-life-cycle-adapted-from-5-6_fig1_345766650

## Slide 18
Summary: Emissions scopes in the stock-flow-service nexus: Overview (general and vehicles)
Service
In-use stocks
Operational (final) electricity and heat
Other energy carriers, materials
Electricity and heat supply
GHG flows
direct emissions or scope 1 emissions
(the two labels mean the exact same thing)
For vehicles: tank-to-wheels TTW
or tailpipe emissions
Indirect emissions or scope 2 emissions associated with electricity and heat supply only
(the two labels mean the exact same thing)
For electric vehicles: well-to-tank WTT
Supply of other energy carriers
Supply of materials
Scope 3 emissions:
‚upstream‘ emissions from energy supply (other than electricity or heat), material production, and other input (water supply, services, precursor products, …)
For gasoline vehicles: well-to-tank WTT

## Slide 19
System boundaries, scopes, & indicators for products...
...must be used consistently!
Product
scope 3 impact
of the product
Energy & heat suppl.
GHG, …
Water
PE
Materials, upstream
GHG, …
Water
PE
Terminology:
Embodied X (PE, Water, GHG, raw materials) of product
=
X Footprint of product
=
cradle (nat. resources) to gate (factory gate) X of product
=
X(scope 3)
End-of-life, waste mgt. and recycling CAN be included, would then be “cradle to grave/cradle to cradle).
 Footprint estimates must disclose their system boundaries!
NOT: life cycle X of product (lacks use phase)
Manufac-turing
GHG, …
Water
PE
Mining, extraction
GHG, …
Water
PE
scope 3 impact
of the product
scope 3 impact
of the product
scope 3 impact
of the product

## Slide 20
System boundaries, scopes, and indicator names...
We have more names/labels than different meanings
In particular, the concept of resource or emissions footprints simply refers to the embodied resources or emissions of a product or service (sum of all resource or emissions flows that cross the boundary of the respective product system of the product or service)
Major differences in indicators still exist related to the system boundary:
  Which upstream processes (e.g., oil extraction, concrete for steel plants to supply material for power station, …) are included?
  Is the infrastructure (roads, railways, …) included or just the vehicle life cycle?
  To what extent is recycled material used (and recycling processes part of the product system)?
 Footprint estimates must disclose their system boundaries!
 Explicit MEFA system definitions are part of scientific footprint estimates!

## Slide 21
Specific terminology for material footprints:
MEFA system definition and calculations
https://www.blog.industrialecology.uni-freiburg.de/index.php/2022/04/20/material-flow-accounting-and-material-footprints-system-definition-and-data-sources/
Relevant indicators:
DE: domestic extraction used (amount of raw materials extracted from national territory for direct use)
I: Imports = direct raw and engineering material input from trade (dry weight at border)
E: Exports = raw and engineering material amounts exported (dry weight at border)
Raw material consumption (RMC), also called ‘material footprint’ (MF) of all goods and services in a country:
measures the total amount of raw materials required to produce all goods and services consumed
MF = RMC = DE + raw material equivalent of all imports RME(I) - raw material equivalent of all exports RME(E).

## Slide 22: Additional material: Urban GHG accounting

## Slide 23
Urban GHG accounting
Source: Pichler et al. (2017), DOI https://doi.org/10.1038/s41598-017-15303-x
GHG Scopes 1 (direct/territorial), 2 (indirect electricity and heat), and 3 (other indirect,
global supply chains) apply to cities as well!
Territorial emissions include the entirety
of emissions that occur within the
city boundary. These are direct emissions
from production (goods & services,
transport) and final consumption
(households, government, investments/
gross fixed capital formation). They also
include urban production for exports.
The GHG footprint, instead, includes
direct and upstream GHG emissions
from household consumption, public
spending, and investment.
The former occur within the city boundary,
the latter may occur anywhere in the world.

## Slide 24
Urban GHG accounting
Source: World Bank (2021) GHG EMISSIONS INVENTORIES: AN URBAN PERSPECTIVE,
available as 210506-Gap-Fund-Technical-Note-1-GHG-Inventory.pdf
GHG Scopes 1 (direct/territorial), 2 (indirect electricity and heat), and 3 (other indirect,
global supply chains) apply to cities as well!

## Slide 25
Urban GHG accounting
Source: World Bank (2021) GHG EMISSIONS INVENTORIES: AN URBAN PERSPECTIVE,
available as 210506-Gap-Fund-Technical-Note-1-GHG-Inventory.pdf

## Slide 26
Urban GHG accounting
Source: World Bank (2021) GHG EMISSIONS INVENTORIES: AN URBAN PERSPECTIVE,
available as 210506-Gap-Fund-Technical-Note-1-GHG-Inventory.pdf

## Slide 27
Urban GHG accounting: Examples
Source: Pichler et al. (2017), DOI https://doi.org/10.1038/s41598-017-15303-x

## Slide 28
Urban GHG accounting: Examples
Source: Pichler et al. (2017), DOI https://doi.org/10.1038/s41598-017-15303-x

## Slide 29
Urban GHG accounting – coming up next:
Energy and GHG embodied in construction
materials (‘grey energy’, ‘grey emissions’)
Source: https://www.researchgate.net/figure/Single-family-and-multi-family-house-Embodied-energy-for-construction-and-maintenance_fig4_335676653
As buildings become more energy efficient, the relevance of the construction phase emissions increases and needs proper assessment and mitigation (lower cement content of concrete, wood as construction material where available, lightweight buidling design, more compact buildings, lower floorspace per capita).
Passive house
(rough indication,
no data)