## Slide 1
Industrial Ecology open online course (IEooc)
Part II: Methods
Methodology 2: Basics of material flow analysis (MFA)
IEooc_Methods2_Lecture5
Carbon accounting and indicators
Stefan Pauliuk, University of Freiburg, Germany

## Slide 2: AFOLU sector and products Carbon accounting – overview and standardisation

## Slide 3
Reporting and accounting of LULUCF activities
“Reporting of land use, land use change and forestry (LULUCF) activities under the
Kyoto Protocol refers to providing information, including estimates of the changes
in carbon stocks and anthropogenic greenhouse gas emissions by sources and removals
by sinks from the following LULUCF activities:
  Activities under Article 3, paragraph 3, and,
  Activities under Article 3, paragraph 4 (mandatory and elected, if any)
in accordance with Article 5, paragraph 2, of the Kyoto Protocol.
Accounting of LULUCF activities under the Kyoto Protocol refers to applying the guidance
contained in decision 16/CMP.1: (in the first commitment period) or decision 2/CMP.7:
(in the second commitment period).”
https://unfccc.int/topics/land-use/workstreams/lulucf-under-the-kyoto-protocol/reporting-and-accounting-of-lulucf-activities-under-the-kyoto-protocol
VERY technical stuff, we keep it simpler while keeping the essence…

## Slide 4
Reporting and accounting of LULUCF activities
“In the LULUCF sector anthropogenic emissions of greenhouse gases (GHG) are reported,
which result from Land Use, Land-Use Change and Forestry.
Emissions from agricultural activities are reported separately.
The inventory distinguishes emissions of carbon dioxide (CO2), methane (CH4),
and nitrous oxide (N2O) from the land-use categories forest land,
cropland, grassland, wetlands, settlements, and other land and from the pools organic
and mineral soils, above-ground and below-ground biomass, deadwood and litter.
Furthermore, the carbon stock in harvested wood products is reported as well as emissions
from artificial waterbodies, wildfires, and industrial peat extraction.
In the LULUCF sector, pools can act both as a source (release → positive emissions)
of greenhouse gases and as a sink (carbon capture → negative emissions) for CO2.”
https://www.thuenen.de/en/thuenen-topics/climate-and-air/emission-inventories-accounting-for-climate-protection/treibhausgas-emissionen-durch-landnutzung-landnutzungsaenderung-und-forstwirtschaft-lulucf

## Slide 5
Example: Germany’s LULUCF emissions
https://www.thuenen.de/en/thuenen-topics/climate-and-air/emission-inventories-accounting-for-climate-protection/treibhausgas-emissionen-durch-landnutzung-landnutzungsaenderung-und-forstwirtschaft-lulucf

## Slide 6
Reporting and accounting of harvested wood products
“Harvested wood products (HWP) include all wood material (including bark) that leaves
harvest sites. Slash and other material left at harvest sites should be regarded as dead organic
matter in the associated land-use category and not as HWP.
HWP constitutes a carbon reservoir. The time carbon is held in products will vary depending
on the product and its uses.
For example, fuelwood and mill residue may be burned in the year of harvest; many types of
paper are likely to have a use life in uses less than 5 years which may include recycling of paper;
and sawnwood or panels used in buildings may be held for decades to over 100 years.
Discarded HWP can be deposited in solid waste disposal sites where they may persist for
long periods of time.”
“All CO2 released from HWP is included in the AFOLU Sector.
CO2 released from wood burnt for energy in the Energy Sector is not included there…”
Questioned by some actors to provide incentive for accounting for carbon storage
in the building sector!
2006 IPCC Guidelines for National Greenhouse Gas Inventories, Chapter 12: Harvested Wood Products

## Slide 7: AFOLU sector and products Carbon accounting – MEFA approach

## Slide 8
System definition for the life cycle of carbon in the technosphere:
Carbon balance of forests and wood use
Flows and stocks
in a given scenario:
„Counter-scenario“:
material substitution
and avoided GHG
Source: Own illustration

## Slide 9
Scientific consensus: We need a combined system definition of forestry and the use phase to fully account for
the carbon impact of wood use!
F_01(t): (net) carbon removal of forests from atmosphere. Can be negative (forest fires, …)
F_12(t): harvested wood into long-lived wood products, C emissions happens after use.
F_13(t): harvested wood into short-lived wood products or energy use, C emissions happens within the same year.
F_30(t): release of biogenic carbon back to the atmosphere after use in techno-sphere.
Net effect of the wood use system (so-called wood use cascade) on climate:
F_01(t) – F_30(t)
 Irrespective what happens within the system, the atmosphere ‚sees‘ only the net effect, F_01(t) – F_30(t).
Carbon balance of forests and wood use

## Slide 10
Consistency of research questions, system definition,
and indicators in the carbon balance of forests & wood use
Research questions for the net climate impact of wood use, relevant for assessing the policy targets for the contribution of forests and wood use to GHG emissions and their reduction.
RQ: What is the net contribution of forests and wood use to GHG emissions?
System perspective: Actual emissions and future scenario for actual emissions
(with uncertainty) from the forestry+technosphere system
System definition: only the upper part of the scheme above: "Forests + techno-sphere" with C flows a and b
Main indicator: Net carbon balance, as net sequestration, actual flows, t of C/yr: a-b or F_0_1 - F_3_0
Cost analogy: This indicator tells about the actual costs of an action that are actually booked on your account. (Here, the carbon 'costs' as atmospheric carbon load, which enters the total GHG emissions statistics)
Application: The net carbon balance is the actual carbon flow that characterizes the net impact of the system on the Earth's climate.

## Slide 11
Consistency of research questions, system definition,
and indicators in the carbon balance of forests & wood use
Research questions for the impacts that are avoided when wood is being harvested and used.
RQ: How much GHG emissions are avoided when wood is being
harvested and used as energy carrier or material?
System perspective: Actual emissions and future scenario for actual emissions
(with uncertainty) from the forestry+technosphere system PLUS the avoided
GHG from NOT producing other energy or materials, + the foregone carbon sequestration if no wood is harvested from forests.
System definition: The upper part AND the lower part of the scheme above: "Forests + techno-sphere" with C flows a and b AND the "substituted/foregone flows" with C flows d and c.
Main indicator: carbon avoided – carbon emitted = c - b + a - d
Cost analogy: This indicator tells about the cost savings (compared to an alternative) that the currently chosen alternative brings. These savings only exist in the comparison to another alternative and are never booked on your account. Same for climate policy: The savings don't matter for the actual climate, they cannot be added to national emissions inventories.
Application: ’Avoided carbon’ tells us whether the chosen scenario is actually more climate-beneficial than the alternatives:
If Carbon avoided - Carbon emitted is negative, the avoided carbon emissions are smaller than the actual ones in the baseline scenario (material or energy use), and the non-harvest alternative would perform better in terms of the climate.
If Carbon avoided - Carbon emitted is positive, the avoided carbon emissions are larger than the actual ones in the
baseline scenario (material or energy use), and the harvest alternative performs better in terms of the climate.

## Slide 12
Carbon balance of forests and wood use
Important disclaimer: Claims on climate neutrality of wood products, like „net zero“ / “biogenic carbon is climate neutral“: These are indicators that are actually based on an underlying MEFA system, and are thus a systems property, not a process or product property!
 Claims on climate neutrality must be transparently linked to the underlying system of quantifiation, if they are not, these claims are not science-based!
Both approaches complement each other:
Actual emissions from the forestry+technosphere system and their future development
are quantified when addressing the RQ:
What is the net contribution of forests and wood use to GHG emissions?
To complement the calculation of the net effect,
the avoided additional carbon sequestration in forests,
the avoided emissions from (fossil) energy supply to sustitute bioenergy,
and the avoided emissions from material production (steel and cement)
are estimated and be used to compare two alternative scenarios.

## Slide 13: AFOLU sector and products Carbon accounting – Timing of sequestration and emission

## Slide 14
Time in the carbon balance of forests and wood use
Timing of emissions is relevant: slow carbon uptake by forests (regrowth)
Time delay of CO2 from burning wood through material use also relevant
Net sequestration possible: Long-term material use PLUS forest regrowth
Does ‚life cycle carbon neutral‘ also mean climate neutral?
Need to properly consider the timing of the C flows and their contribution
to global warming up to a given time horizon!

## Slide 15
GHG timing: Fate of a CO2 pulse emission in the atmosphere
Order/ Variable | 0 | 1 | 2 | 3
a | 0,2173 | 0,2240 | 0,2824 | 0,2763
τ | --- | 394,4 | 36,54 | 4,304
Sources: Numbers and equations are taken from: “Anthropogenic and Natural Radiative Forcing”, Table 8.A.1 in part I of the 5th IPCC
Assessment report, and from: “Anthropogenic and Natural Radiative Forcing, Supplementary Material”, Section 8.SM.11.1:
Equations for the Global Warming Potential of part I of the 5th IPCC Assessment report
CO2 is a stable compound in the atmosphere, but it is dissolved in water (especially in the oceans) as hydrogen carbonate
and increasingly stored in biomass (forests). The following partial decomposition of an emission pulse at t = 0 was determined,
shown as a proportion R(t) of the original emission (corresponds to 100%):
Unit: 1
Unit: yr
Decay curve Ri(t)
Ri(t) for carbon dioxide (CO2)
 So-called Bern carbon cycle model

## Slide 16
GHG timing: Decay of methane in the atmosphere
The reaction above has a certain probability of occuring during a given time interval, which leads to exponential decay
of the substance with a given average lifetime:
The following equation shows the fraction of an original
pulse emission at t = 0:
For other greenhouse gases, like N2O, fluoro- and chloro-
organic carbons, the same decay relation holds, just the
Atmospheric lifetime of each gas is different.
Sources: Numbers and equations are taken from: “Anthropogenic and Natural Radiative Forcing”, Table 8.A.1 in part I of the 5th IPCC
Assessment report, and from: “Anthropogenic and Natural Radiative Forcing, Supplementary Material”, Section 8.SM.11.1:
Equations for the Global Warming Potential of part I of the 5th IPCC Assessment report
Unit: 1
Unit: yr
Ri(t) for methane (CH4)
Decay curve Ri(t)

## Slide 17
GHG Timing: Converting different GHG into CO2-equivalents
Different GHG have different residence time in the atmosphere
and they absorb infrared radiation at different rates  how to compare different GHG?
GWPx,T: global warming potential of substance x with a time horizon T
ax: radiative efficiency due to a unit increase in atmospheric abundance
of the substance in question (i.e., W/(m2∙kg), ‘effectiveness of GHG’
[x(t)] is the time-dependent concentration of substance x,
ar, [r(t)]: effectiveness and concentration of reference gas (CO2)
GWPx,T x T | 20 year, ‘individualist’ | 100 year, ‘hierarchist’ | 500 years ‘egalitarian’
CO2 | 1 | 1 | 1
CH4 | 72 | 25 | 7.6
N2O | 289 | 298 | 153
SF6 | 16300 | 22800 | 32600
Recommended reading: https://www.researchgate.net/publication/302559709_ReCiPE_2008_A_life_cycle_impact_assessment_method_which_comprises_harmonised_category_indicators_at_the_midpoint_and_the_endpoint_level
Application in MEFA: CO2-equivalent (GHG) = mass (GHG) * GWP (GHG,T)

## Slide 18
GHG emissions of a system over time: timing matters!
Figure 1 from Levasseur et al. (2010): Illustration of the inconsistency in time frames for global warming LCIA with the example of a 75-year lifetime building.
To establish consistency, the time horizon for each GHG pulse emissions in a given year is set so that the impact on global warming is accounted for only until the time horizon of the entire analysis.
For example, if a maintenance-related emissions occurs at year 60, it contributes to the total GWP only with a time horizon of 100 – 60 = 40 years.
Approach: We don’t have a fixed GWP factor for each GHG, but a GWP factor for each year of emissions, and that factor
is calculated with a rolling time horizon.
Source: Figure 1 from Levasseur et al. (2010): Considering Time in LCA. Environmental Science & Technology 44(8): 3169–3174.

## Slide 19
Application to GHG timing: Carbon sequestration & storage
Chart: Carbon balance: Energy use (blue) vs. material use (red), plus forest regrowth (grey)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Logging yr 0, instantaneous burning, energy use | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Logging yr 0, material use 50 yr, burning | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 0 | 0 | 0 | 0
Forest carbon sequestration after logging, regrowth | 0 | -0.5 | -1 | -2 | -3 | -2 | -1 | -0.5 | 0 | 0 | 0
Chart: Net CO2 in atmosphere, time t after biomass harvest
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Logging yr 0, inst. burning, energy use | 10 | 6.0841 | 4.2951 | 2.393 | -0.51556 | -1.4959 | -1.5528 | -1.3765 | -0.91296 | -0.68781 | -0.54788
Logging yr 0, material use 50 yr, burning | 0 | -0.5 | -1.3292 | -2.6228 | -5.13 | 4.1676 | 0.8985 | 0.27314 | 0.25738 | 0.19155 | 0.15085
tons of carbon (C)
tons of carbon (C)
yr
yr
Carbon flows in from/to system
Blue and red are two alternatives
Carbon stocks in atmosphere
Blue and red are two alternatives
Consider the situation where a patch of forest is clear-cut for wood harvest in year 0. The harvested wood is used either for heating (so that the carbon in the wood is released in the same year, blue scenario) or as construction material (so that the carbon in the wood is released after 50 years, red scenario).  See plot on the left side.
GWP: Ca. 30% of fossil CO2
GWP: Ca. -7% of fossil CO2
For details, see IEooc_Methods4_Exercise11 on https://www.industrialecology.uni-freiburg.de/teaching
After clear-cutting, the forest slowly regrows, leading to a carbon sequestration from the atmosphere as shown by the grey bars on the left side. Right side: carbon stock in the atmosphere, calculated from the flows on the right side and the Bern carbon cycle model (see slide above).

## Slide 20
Application to GHG timing: Carbon sequestration & storage
Chart: Carbon balance: Energy use (blue) vs. material use (red), plus forest regrowth (grey)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Logging yr 0, instantaneous burning, energy use | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Logging yr 0, material use 50 yr, burning | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 0 | 0 | 0 | 0
Forest carbon sequestration after logging, regrowth | 0 | -0.5 | -1 | -2 | -3 | -2 | -1 | -0.5 | 0 | 0 | 0
Chart: Net CO2 in atmosphere, time t after biomass harvest
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Logging yr 0, inst. burning, energy use | 10 | 6.0841 | 4.2951 | 2.393 | -0.51556 | -1.4959 | -1.5528 | -1.3765 | -0.91296 | -0.68781 | -0.54788
Logging yr 0, material use 50 yr, burning | 0 | -0.5 | -1.3292 | -2.6228 | -5.13 | 4.1676 | 0.8985 | 0.27314 | 0.25738 | 0.19155 | 0.15085
tons of carbon (C)
tons of carbon (C)
yr
yr
Carbon flows in from/to system on last slide.
Blue and red are two alternatives
Carbon stocks in atmosphere
Blue and red are two alternatives
When converting atmospheric carbon flows to stocks (left to right plot), the Bern carbon cycle model is used.
Bars in right plot are proportional to momentary/instantaneous radiative forcing of GHG from system.
Total radiative forcing is calculated as the sum of momentary forcing until the time horizon (100 yr) (sum of all red or all blue bars in the right plot).
The GWP of the two alternatives is calculated as the ratio of the total radiative forcing calculated from the
right figure and the total forcing of a CO2 pulse of the same size as the harvest flow in year 0 (reference flow).
GWP: Ca. 30% of fossil CO2: Forest regrowth
partly compensates for emission pulse at year 0.
GWP: Ca. -7% of fossil CO2: Storage of carbon
in buiding materials leads to net negative impact!
For details, see IEooc_Methods4_Exercise11 on https://www.industrialecology.uni-freiburg.de/teaching