## Slide 1
Industrial Ecology open online course (IEooc)
Part II: Methods
Methodology 4: Life Cycle Assessment
IEooc_Methods4_Lecture1
The computational structure of LCA
Stefan Pauliuk, University of Freiburg, Germany

## Slide 2
Summary: LCA in one equation

## Slide 3
Inventory of an industrial process
Primary steel production,
Company X
Germany, 2013
10 Mt steel
2.8 Mt CO2
3 Mt slag
Main product:
Emissions/
Waste:
Precursor
products
Natural
resources
2.6 Mt O2
15 Mt iron
ore
9.45 Mt Coke
1.8 TWh Electr.
4 Mt Limestone
Flows are recorded in ‘natural’ physical unit, using data from company records
and process models
Accounting on multiple physical layers, therefore only basic mass and energy
balance checks possible.
System boundary: Integrated steel mill of company X, Duisburg, Germany
annual total, 2013

## Slide 4
The basic process model of LCA: The unit process
Unit Process:
Primary steel production,
Germany, 2008
1 t steel
2.8 t CO2
300 kg slag
Main product:
Emissions/
Waste:
Precursor
products
Natural
resources
260 kg O2
1.5 t iron
ore
945 kg Coke
1800 kWh Electr.
400 kg Limestone
Each industrial process is assigned one main product.
Flows are recorded in ‘natural’ physical unit.
Accounting on multiple physical layers.
Take process inventory and normalize it to 1 unit of main product
(here: by dividing all flows by 10 million)

## Slide 5
 | Object | Unit | Steel production: 1 tonne of steel
Resources | Iron ore | t | 1.5
 | O2 | kg | 260
 | Coal | t | 0
 | Limestone | kg | 400
Products | Coke | kg | 945
 | Electricity | kWh | 1800
 | Steel | t | 0
Ems. | CO2 | t | 2.8
 | Slag | kg | 300
Vector representation of the basic LCA process model
Unit Process:
Primary steel production,
Germany, 2008
1 t steel
2.8 t CO2
300 kg slag
Main product:
Emissions/
Waste:
Precursor
products
Natural
resources
260 kg O2
1.5 t iron
ore
945 kg Coke
1800 kWh Electr.
400 kg Limestone
All flows recorded in one column, except for main product
Different flow groups (pre-products, resources, and emissions) are grouped into sections

## Slide 6
Modelling the global socioecological system
http://dx.doi.org/10.1016/j.gloenvcha.2013.11.006

## Slide 7: Recap: LCA concepts and definitions refresh
Functional unit: quantitative description of the service provided by industrial
output to the end user
 Example: 1000 km drive with electric passenger vehicle, standard driving cycle
Reference flow: Amount of industrial products that is necessary to deliver the
service described in the functional unit.
 Example: supply, use, and disposal of 0.005 electric vehicles (200 000 km total), 200 kWh
Product system: Part of the economy that delivers the reference flow.
Example: Production und final disposal of 0.005 electric vehicles, electricity generation
and distribution
Life cycle inventory: All flows within the product system and between product system
and environment
Emissions/Resources: Flows of material and substances between the natural env.
and the product system (ore, timber, water, CO2, Hg, …)
Goal&scope phase
Life cycle inventory (LCI) phase

## Slide 8
Objects and process groups in LCA, part 1
Name | Type | Example
Services | Often immaterial flows from devices to people | Thermal comfort, light, transport
Products (aka commodities) | Industrially produced stuff | Fuel, cars, food, electricity
Emissions and Resources ‚elementary flows‘ | Stuff that nature supplies or absorbs | Ore, Timer, GHG emissions, slag
Objects
Name | Type | Example
Society | Agents | People, governmt.
Households | Transformation proc. | HH, public institut.
Markets | Distribution process | Electricity market
Industries | Transformation proc. | Steel industry
Process groups

## Slide 9
Computational structure of LCA: The functional unit
f
Functional unit f:
“quantified performance of a product
system for use as a reference unit” (ISO)
“quantitative description of the service
provided to the consumer and investigated
by the study
f is a column vector [#services x 1]

## Slide 10
Computational structure of LCA: Service intensity and reference flow
f
Service intensity S and reference flow y:
Reference flows describes commodities
needed to provide service described by
functional unit.
Service intensity matrix converts services
into commodities
y
S
y is a column vector [#commodities x 1]
S is a matrix [#commodities x #services]

## Slide 11
Relation between reference flow and functional unit

## Slide 12
Modelling the product system by hand
Combining unit processes to model the product system,
step by step
Unit Process:
Primary steel production,
Germany, 2008
1 ton of steel
2.8 tons of CO2
300 kg slag
Main product:
Emissionen/
Waste:
Inputs
Natural
resources
260 kg O2
1.5 tons of
iron ore
945 kg Coke
1800 kWh El
400 kg Limestone
Process 1
Process 2
Process 3
Process 4
Process 5
Process 7
Process 6
Notes: 12

## Slide 13
Product system
Car production
Electricity generation
Car shredder
service
Reference flow
Graphical modeling of the product system
Advantages:
  Simple and intuitive method
  Widely applied, especially in industry
  Graphical representation of the product system
Disadvantages:
  Where to stop? (Cut-off)
  Messy after several steps already
  Bulky if many processes are involved
  Many processes apear over and over again (electricity supply)
Building the product system by hand: Why and why not do it?

## Slide 14
 | Object | Unit | Steel production (1 ton of steel) | Electricity generation (1 kWh of electricity) | Coke production (1 kg Coke)
Resources | Ore | t | 1.5 | 0 | 0
 | O2 | kg | 260 | 0.85 | 0.18
 | Coal | t | 0 | 0.00035 | 1.34
 | Limestone | kg | 400 | 0.03 | 0
Products | Steel | t | 0 | 0 | 0
 | Electricity | kWh | 1800 | 0.15 | 0.1
 | Coke | kg | 945 | 0 | 0
Ems. | CO2 | t | 2.8 | 0.0012 | 0.23
 | Slag | kg | 300 | 0.00004 | 0.07
Resources R
Inter-industry usage A
Emissions B
Products
Products
r x p
p x p
b x p
Format
Matrix representation
of the product system
The solution: The product system as matrix

## Slide 15
Each industry is assigned a fixed column position/column index
Each industry is assigned a main product (steel production  steel) and vice versa
The corresponding product is assigned a fixed row position/row index
For each product a consistent single unit is used across the entire table
This unit is at the same time the unit of the reference product for its assigned industry
All common inputs (electricity, chemicals, metals, transport) is taken from special
databases with generic process data (GaBi, ecoinvent) ‘background databases’
Project- or plant-specific processes are recorded separately from the background data
The solution: The product system as matrix

## Slide 16
Computational struct. of LCA: industry output and technical coefficients
f
Industrial output x and matrix of tech-
nical coefficients A:
Industrial output x contains output of
commodities in different industrial procs.
(entire supply chain output)
The matrix of technical coefficients A
contains the production ‘recipes’ of all
industrial processes in the value chain.
y
S
A is a matrix [#commodities x #industries]
x
A·x
^
x is a column vector [#commodities x 1]

## Slide 17
f
Diagonalized industrial output x
and matrix of commodities-to-industry
flows Z:
To suppress summing up over the different
Products in x we put each product on a
separate column. A·x then gives the
matrix of commodity-by-industry flows Z.
y
S
Z is a matrix [#commodities x #industries]
x
A·x
^
Computational struct. of LCA: industry output and technical coefficients
X is a matrix [#commodities x #commodts.]
^
^

## Slide 18
Constructing the product system with the A-matrix
With the help of the market balance, the product system can be built step by step.
Step | Final demand | Industry output | Intermediate de-mand for next step
0 | y | x0=I·y | A·y
1 |  | x1=A·y | A2·y
2 |  | x2=A2·y | A3·y
3 |  | x3=A3·y | A4·y
4 |  | x4=A4·y | A5·y
… |  | … | …
∞ |  | x=L·y | 
Every power of A represents
one tier in the supply chain!
Reference: http://www.lcatextbook.com/ Chapter 8, provided on ILIAS
If the power series of I+A+A2+A3+A4+… converges, it can be rewritten as follows:
Nat. resources/
Emissions 
L is called ‚Leontief inverse‘.

## Slide 19
A more technical derivation of the Leontief L matrix
With the help of A, the market balance can be reformulated (e is a summation vector of 1s only)
 Market balance in terms of x, y, and A
 Inverted market balance, L is called ‚Leontief inverse‘.
Nat. resources/
Emissions 
 Market balance with flow vectors and tables

## Slide 20
Mixed units are no problem for A and L, they are preserved under inversion!
If the IOT has mixed units, A, A2, A3, A4, … and L also have mixed units. That is no problem.
[L] denotes the units (of measurement) of L. Same for A.
Remember that no column balances can be calculated in a mixed unit system.

## Slide 21
f
Matrix of relative emissions by industry B
and vector of total emissions b:
b= B·x
y
S
B is a matrix [#emissions x #industries]
x
A·x
^
Computational structure of LCA: Emissions
b is a vector [#emissions x 1]
B

## Slide 22
Reference flow
Leontief-IO-Model
of the industrial network
Emission coefficients
(emissions per unit of
industrial output)
Emissions of the
product system
The life cycle inventory in a single equation

## Slide 23
End result, emissions to the environment b:
((I - A)-1 is called ‚Leontief-inverse‘ symbol: L)
b = B ∙ (I - A)-1 ∙ y
The life cycle inventory stage in one line
Reference: http://www.lcatextbook.com/ Chapter 8

## Slide 24
Parts 3: environmental mechanisms
http://dx.doi.org/10.1016/j.ecolecon.2015.08.012

## Slide 25
Objects and process groups in LCA, part 2
Name | Type | Example
Emissions and Resources | Stuff that nature supplies or absorbs | Ore, Timer, GHG emissions, slag
Environmental midpoints | Characterisation factor (state or change of state) | Contribution to Global warming or acidification
Environmental endpoints | Characterisation factor (state or change of state) | Human health, Species richness
Objects
Name | Type | Example
Environmental mechanisms type 1 | Transformation process | Global warming, acidification, ozone depletion
Environmental mechanisms type 2 | Transformation process | Damage to human health, biodiversity change
Process groups

## Slide 26
Example for an impact assessment method: ReCiPe 2008
Midpoints reflect direct environmental relevance (waste is not a category!)
Midpoints are defined at the place where mechanisms common to a variety
of substances come into play (radiative forcing, soil base cation saturation)
Impact category indicators are measurable places in an impact pathway.
Per-unit impacts are given by characterisation factors,
which in turn require characterisation models.

## Slide 27
Example for an impact assessment method: ReCiPe 2008
Recommended reading: Goedkoop
et al. (2013): ReCiPe 2008. Provided on ILIAS
18 ‘midpoint indicators’
3 ‘endpoint indicators’

## Slide 28
What is a characterization factor?
The characterization step of LCIA quantitatively transforms each set of classified
inventory flows via characterization factors (also called equivalency factors) to create
impact category indicators relevant to resources, ecosystems, and human health.
Reference: http://www.lcatextbook.com/ Chapter 10
A characterisation factor is a biophysical
quantity that indicates the impact on a
certain environmental mechanism
per unit of emissions or resource extraction.

## Slide 29
f
Matrix of characterization factors C
and vector of midpoint indicators c
c = C·b
y
S
C is a matrix [#mechanisms x #emissions]
x
A·x
^
Computational structure of LCA: Environmental mechanisms
c is a vector [#emissions]
B
C

## Slide 30
f
Damage factor matrix D and total
damage (endpoints) h:
h = D·c
y
S
D is a matrix [#endpoints x #midpoints]
x
A·x
^
Computational structure of LCA: Damage and damage coefficients
h is a vector [#endpoints]
B
C
D
h

## Slide 31
An LCA in one line
Environmental impacts c of a reference flow y on the midpoint level:
c= C ∙ B ∙ (I - A)-1 ∙ y
C: characterization factors, B: emissions, A: inter-industry requirements,
y: reference flow
Reference: http://www.lcatextbook.com/ Chapter 10

## Slide 32
The whole picture
damage
Characterisation
Factors midpoints
Reference flow
Leontief-IO-Model
of the industrial network
Emission coefficients
(emissions per unit of
industrial output)
Characterisation
factors endpoints

## Slide 33
4. Summary: LCA in one equation

## Slide 34
5. Comparison to Heijungs and Suh (2002)
Here, the Leontief input-output model was used to derive total industrial output
of the supply chain for a given exogenous final demand y.
In their book “Computational structure of Life Cycle Assessment”, Heijungs and Suh
present an alternative approach to scale process inventories to construct a balanced
supply chain model.
It is instructive to compare both approaches as it reveals insights into the system
definition and process model that lies at the basis of this type of process LCA.
If interested, have a look at
IEooc_Methods4_Exercise10: Matrix inversion methods in process-based LCA
(!Notation confusion: Heijungs and Suh also use A and B matrices, but with different meaning!)